## Slide 1: Fast Image/Video Contrast Enhancement Based on Weighted Thresholded Histogram Equalization
EECS 740 Digital Image Processing Project
Lohith

## Slide 2: Outline:
Introduction
  1.A. Histogram
  1.B. Histogram Equalization
  1.C. Types of HE
Technical discussion
Results
Comparative study
Conclusions
Questions & Answers

## Slide 3: 1. Introduction.
1.A. Histogram:
  A Histogram of an image gives information about the distribution of intensity levels.
  A histogram doesn’t provide any information about the spatial distribution of pixels.
1.B. Histogram Equalization:
  Histogram equalization is used to enhance contrast.
  The level mapping equation is where Hk is output level, K is range of gray levels, C(k) is the cumulative distribution function.
  The increment in the output level Hk is,
1.C. Drawbacks:
  It cannot be controlled.
  Unpleasant visual effects such as, over enhancing and increase in noise.

## Slide 4: 1. Introduction
1.C. Types of HE:
1.C.1 Adaptive:
In AHE, equalization is based on the histogram and statistics obtained from the neighbourhood around each pixel.
Adaptive methods provide greater enhancement than global methods but are computationally intensive.
1.C.2 Improved Global methods:
In the improved global methods, various constraints are added to the global equalization or the modification procedures to achieve better performance.
Global methods are computationally feasible and provide images with acceptable quality.

## Slide 5: 2. Technical discussion
The proposed weighted thresholded(WTHE) enhancement method performs histogram equalization based on a modified histogram.
Each original probability density value P(k) is replaced by a weighted and thresholded PDF value Pwt(k)
Pwt(k) is obtained by applying a transformation function Ω(.) to P(k),
The original PDF is clamped at an upper threshold Pu and at a lower threshold Pl and all other values between upper and lower thresholds are transformed using a normalized power law function with index r>0.

## Slide 6: 2. Technical discussion
The increment for each intensity level can be controlled by adjusting the index r of the power law transformation function.
Ex: When r<1, higher weights are given to low probabilities than the high probabilities. i.e, the less-probable levels are protected and over-enhancement is less likely to occur.
Also, there is an upper limit Pu as a result, all levels whose PDF values are higher then Pu will have the increment clamped at a max.
The value of Pu is decided by v is a real number which defines the upper threshold normalized to Pmax .
The lower threshold Pl is only used to cut out the levels whose probabilities are too low( little visual importance).
We can also observe that when r=1, Pu=1 and Pl=0, the WTHE method reduces to traditional HE.

## Slide 7: 2. Technical discussion
After the weighted thresholded PDF is obtained the cumulative distribution function(CDF) is obtained by
The HE procedure is,
Wout is the dynamic range of output image, Madj is the mean luminance level after enhancement.
Video Enhancement:
The proposed WTHE enhancement method is applied to the luminance component of the video, leaving chrominance components unchanged.
The equation for WTHE introduces enhancement gain control that constraints the ratio between the output and input dynamic range.

## Slide 8: 2. Technical discussion
Win is the dynamic range of the input image and Gmax is a pre-set maximum gain of dynamic range. Enhancement gain control is especially useful for scenes that have narrow or gradually changing dynamic ranges.
Madj is the mean adjustment quantity that reduces the luminance changes after enhancement. To decide on the value of Madj, we first calculate the mean of the enhanced image F hat(i,j) assuming Madj =0.
Then the difference between it and the mean of the original image is calculated. Madj is set equal to the value closest to this mean difference such that it does not cause serious level saturation (clipping).

## Slide 9: 3. Results

## Slide 10: 4. Comparative study

## Slide 11: 5. Conclusions